Just in Time Training

For Hospitals

PPE and Wet Decontamination

Using Level C Gear

Equipment and Supplies

For Ambulatory Decon

- Bull horn or PA

- White board & dry erase markers

- Medical evaluation sheets with clipboards

- BP equipment

- PAPRS

- Boots

- Gloves

- Booties

- Suits

- Duct Tape

- Scissors

- Buckets & Soft Brushes

- Redress kits

- Towels

- Trash bags

- Permanent markers

Pre-Decon Activities

- Try to calm the person

- Tell them what is going to happen in the tent

- Protect their modesty as best you can

- Help them undress

- Give them their redress kit

- Help them to bag their clothes in the bio-bag

- Collect valuables, help them to put them into the bag

- Mark the bags

- Direct them into the Tent (or other decon area)

PAPR Donning

- Dress in scrubs or other clothing suitable for maintaining a comfortable body temperature.

- Remove all jewelry and place in a secure place.

- Persons with long hair must pull it back and secure it away from face.

- Hydrate with 8-16 ounces of fluid

- Take blood pressure, pulse and respiration.

  - Record on the Medical Evaluation form.

- Obtain appropriate sized PPE (suit, gloves and boots)

- Obtain PAPR with battery and 3 cartridges.

- Tear tape, 2 pieces for wrist, 2 for legs, 1 for zipper & 1 for name tag.

- Lay out PPE and inspect them for damage.

- Apply cartridges and test PAPR

- Put on inner gloves.

- While sitting, remove shoes if not done already.

- Pull on protective suit to waist

- Put on outer boots and tape in place.

Continued…

PAPR Donning

Continued

- Place arms in sleeves. Put on outer gloves and tape.

- Zip front of suit ¾ of the way. Place tape on zipper ¾ of the way up.

- Connect PAPR hood to blower and turn on. Snap belt around the waist.  Air hose should go over the shoulder not under.

- Ensure there is good air flow after the hood is on.

- Place hood on and tuck in inner hood, zip suit up the rest of the way

- Tape zipper rest of the way.

- Adjust hood for comfort and good visibility

- Exchange thumbs-up approval signals before proceeding.

- Place name tag and time on the back of the suit.  (e.g. Bluschke 0830)

Decontamination

- Make eye contact, talk to them if you can

- Use hand signals to motion then to come toward you,

then signal them where to stop

- Spray them from top to bottom front to back

- Tell them to lift their arms

- Wash, rinse, Then wash, rinse again.  (may use soaps)

- Help walk the person through the tent

- Assist them until they are with someone in the cold zone

* If non ambulatory, spray top to bottom, front to back

Then tip them to wash the back side

If on a backboard or other aid, wash those too.

Post-Decon Activities

Caring for those who have finished decontamination

Providers are in the clean zone

May wear street clothes, scrubs etc.

- Protect privacy of victims as much as possible

- Help them to dry off

- Help them into their re-dress covers

- Reassure, and try to calm them

- Explain the process for possible recovery of their valuables

- Direct them to the next area for warmth and assessment

# PAPR Doffing

- Wash gloved hands thoroughly.

- Still wearing PPE, self-wash, starting at the top of the head and working down to the bottom of the boots.

- Have a partner wash your back.

- Untape boots and gloves, but do not remove them.

- Unlock PAPR and place it on chair/gurney/floor, etc.

- Remove the outer suit—roll the suit away from you, inside out (with help from a partner).

- Remove outer gloves along with the outer suit.

- Step out of boots and suit into final rinse area (keep inner gloves and clothing on).

- Remove PAPR hood, clean & store.

- Wash and rinse thoroughly (with partner’s help).

- Remove (inner) suit, place in waste.

- Remove inner gloves: first pinch one glove and roll it down partially, then place thumb in other glove & remove both gloves simultaneously.

- Wash again, removing inner clothing, then step out of decontamination shower and into towels/blankets.

- Dress and report for final medical evaluation.